## Slide 1: ΕΝΕΡΓΕΙΑΚΗ ΠΟΛΙΤΙΚΗ ΚΑΙ ΔΙΑΧΕΙΡΙΣΗ - ΛΗΨΗ ΑΠΟΦΑΣΕΩΝ
ΔΙΑΛΕΞΗ Νο 06
ΔΙΑΛΕΞΗ Νο 07
ΕΝΕΡΓΕΙΑΚΕΣ ΤΕΧΝΟΛΟΓΙΕΣ

## Slide 4: Συντελεστές Μετατροπής
Βασικές Μονάδες Ενέργειας
1 Joule (J) = 0.2388 cal
1 calorie (cal) = 4.1868 J
1 barrel = 42 US gallons = 159 litres (approx.)
1 cubic metre = 35.315 cubic feet = 6.2898 barrels
1 British thermal unit [BTU] = 1.055 kJ = 0.252 kcal
1 tonne of oil equivalent (toe) = 41.868 GJ = 10 000 Mcal
1 tonne of coal equivalent (tce) = 29.3 GJ = 7 000 Mcal
Ηλεκτρισμός
1 kWh ηλεκτρισμού = 3.6 MJ = approx. 860 kcal

## Slide 5: ΕΥΡΩΠΑΪΚΗ ΕΝΩΣΗ: ΠΟΛΙΤΙΚΕΣ-ΚΛΕΙΔΙΑ ΓΙΑ ΕΝΑΛΛΑΚΤΙΚΟ ΣΕΝΑΡΙΟ
ΗΛΕΚΤΡΟΠΑΡΑΓΩΓΗ
  ΟΔΗΓΙΑ ΓΙΑ ΑΝΑΝΕΩΣΙΜΕΣ ΠΗΓΕΣ ΕΝΕΡΓΕΙΑΣ
  ΟΔΗΓΙΑ ΓΙΑ ΣΥΜΠΑΡΑΓΩΓΗ ΘΕΡΜΟΤΗΤΑΣ ΚΑΙ ΗΛΕΚΤΡΙΣΜΟΥ
ΤΟΜΕΑΣ ΜΕΤΑΦΟΡΩΝ
  ΕΘΕΛΟΝΤΙΚΕΣ ΣΥΜΦΩΝΙΕΣ ΜΕ ΑΥΤΟΚΙΝΗΤΟΒΙΟΜΗΧΑΝΙΕΣ: ΕΠΕΚΤΑΣΗ ΚΑΙ ΕΝΤΑΤΙΚΟΠΟΙΗΣΗ
  ΣΤΟΧΟΙ ΒΙΟΚΑΥΣΙΜΩΝ
ΟΙΚΙΑΚΟΣ ΚΑΙ ΕΜΠΟΡΙΚΟΣ ΤΟΜΕΑΣ
  ΟΔΗΓΙΑ ΓΙΑ ΕΝΕΡΓΕΙΑΚΗ ΑΠΟΔΟΣΗ ΚΤΙΡΙΩΝ
  ΕΝΕΡΓΕΙΑΚΗ ΣΗΜΑΝΣΗ ΣΥΣΚΕΥΩΝ (LABELLING)

## Slide 6: ΣΤΑΔΙΑ ΜΕΤΑΤΡΟΠΗΣ
ΣΧΗΜΑΤΙΣΜΟΣ ΚΑΡΒΟΥΝΟ, ΠΕΤΡΕΛΑΙΟ, ΦΥΣΙΚΟ ΑΕΡΙΟ
ΚΟΙΤΑΣΜΑ ΕΝΤΟΠΙΣΜΟΣ ΚΑΙ ΑΞΙΟΛΟΓΗΣΗ
ΕΞΟΡΥΞΗ ΥΛΙΚΑ & ΕΝΕΡΓΕΙΑ - ΠΕΡΙΒΑΛΛΟΝ
ΜΕΤΑΦΟΡΑ ΤΡΕΝΟ, ΦΟΡΤΗΓΑ, ΠΛΟΙΑ, ΑΓΩΓΟΙ
ΕΠΕΞΕΡΓΑΣΙΑ ΜΕΤΑΤΡΟΠΗ, ΕΞΕΥΓΕΝΙΣΜΟΣ
ΚΑΥΣΗ
ΠΑΡΑΓΩΓΗ ΘΕΡΜΙΚΗΣ ΕΝΕΡΓΕΙΑΣ
ΠΑΡΑΓΩΓΗ ΜΗΧΑΝΙΚΗΣ ΕΝΕΡΓΕΙΑΣ
ΠΑΡΑΓΩΓΗ ΗΛΕΚΤΡΙΚΗΣ ΕΝΕΡΓΕΙΑΣ
ΜΕΤΑΦΟΡΑ & ΔΙΑΝΟΜΗ
ΧΡΗΣΗ
ΚΑΛΥΨΗ ΑΝΑΓΚΩΝ ΘΕΡΜΑΝΣΗ, ΜΑΓΕΙΡΕΜΑ, ΦΩΤΙΣΜΟΣ, ΣΥΣΚΕΥΕΣ, ΜΕΤΑΦΟΡΕΣ, ΠΑΡΑΓΩΓΗ ΥΛΙΚΩΝ
ΒΙΩΣΙΜΗ ΑΝΑΠΤΥΞΗ

## Slide 7: Κοσμική ακτινοβολία – η αρχή
Notes: Origin of the cosmic background radiation
About 100,000 years after the Big Bang, the temperature of the Universe had dropped sufficiently for electrons and protons to combine into hydrogen atoms, p + e --> H. From this time onwards, radiation was effectively unable to interact with the background gas; it has propagated freely ever since, while constantly losing energy because its wavelength is stretched by the expansion of the Universe. Originally, the radiation temperature was about 3000 degrees Kelvin, whereas today it has fallen to only 3K.
Observers detecting this radiation today are able to see the Universe at a very early stage on what is known as the `surface of last scattering'. Photons in the cosmic microwave background have been travelling towards us for over ten billion years, and have covered a distance of about a million billion billion miles. The Origin of Fluctuations in the CBR
There are a variety of competing theories for the origin of large-scale structure and the fluctuations in the cosmic microwave background radiation. These models fall into two categories: (1) causal topological defect models, such as cosmic strings and textures, or (2) inflationary scenarios.
Following subtraction of the dipole anisotropy and components of the detected emission arising from dust (thermal emission), hot gas (free-free emission), and charged particles interacting with magnetic fields (synchrotron emission) in the Milky Way Galaxy, the cosmic microwave background (CMB) anisotropy can be seen. CMB anisotropy tiny fluctuations in the sky brightness at a level of a part in one hundred thousand was first detected by the COBE DMR instrument. The CMB radiation is a remnant of the Big Bang, and the fluctuations are the imprint of density contrast in the early Universe (see slide 24 caption). This image represents the anisotropy detected in data collected during the first two years of DMR operation. Ultimately the DMR was operated for four years. See slide 19 caption for information about map smoothing and projection.
24
This image combines data from the DIRBE obtained at infrared wavelengths of 100, 140 and 240 µm - the longest wavelengths measured by this instrument. The sky brightness at these wavelengths is represented respectively by blue, green, and red colors in the image. This image shows where there is more material (appears brighter) and where this material is coldest (appears redder). The plane of the Milky Way Galaxy lies horizontally across the middle of the image with the Galactic center at the center. Most of the infrared radiation seen in this image originates from cold dust (approximately 20 K, or 20 degrees Centigrade above absolute zero) located in clouds of gas and dust between the stars in the Milky Way Galaxy. The wispy-looking dust features are called "infrared cirrus." The region of the Orion Nebula with active star formation approximately 1,500 light years distance from the Sun appears on the right of the image below the plane of the Milky Way. Neighboring galaxies, the Large and Small Magellanic Clouds, appear as faint "blobs" below and slightly to the right of the Galactic center. Much of the picture appears to be the same color, indicating that there is not a large variation in the dust temperature. Because the brightness of the Solar System and Galaxy tends to decrease with increasing wavelength, these long wavelength DIRBE measurements are particularly valuable for searching for the cosmic infrared background.

## Slide 8: ΕΞΕΛΙΞΗ ΠΑΡΑΓΩΓΗΣ ΕΝΕΡΓΕΙΑΣ

## Slide 9: Η ΔΟΜΗ ΤΟΥ ΕΝΕΡΓΕΙΑΚΟΥ ΣΥΣΤΗΜΑΤΟΣ
ΠΗΓΕΣ | ΤΕΧΝΟΛΟΓΙΑ ΜΕΤΑΤΡΟΠΗΣ | ΦΟΡΕΑΣ (νόμισμα) | ΤΕΧΝΟΛΟΓΙΑ ΔΙΑΝΟΜΗΣ-ΜΕΤΑΦΟΡΑΣ | ΤΕΧΝΟΛΟΓΙΑ ΧΡΗΣΗΣ | ΥΠΗΡΕΣΙΕΣ
Πετρέλαιο | Διυλιστήρια | Βενζίνη | Τρένο,τάνκερ | Λέβητας | Θέρμανση
Φυσικό αέριο | Γεωτρήσεις | Πετρέλαιο | Αγωγοί | Λάμπα | Φωτισμός
Κάρβουνο | Ορυχεία | Φυσικό αέριο | Ηλεκτρικές γραμμές | Αιρ Κοντίσιον | Ψύξη
Ηλιακή | Συλλέκτες | Ηλεκτρισμός |  | Τηλέφωνο | Επικοινωνίες
Αιολική | Ανεμογεννήτριες | Θερμότητα |  | Αυτοκίνητο Τρένο, | Μεταφορές
Υδροηλεκτρ. | Φράγματα | Υδρογόνο |  | Κουζίνα | Μαγείρεμα
Γεωθερμία | Γεωθερμικοί σταθμοί |  |  |  | 
Βιομάζα | Σταθμοί καύσης, πυρόλυσης |  |  |  | 
Ουράνιο | Ορυχεία |  |  |  | 

## Slide 10: ΠΑΓΚΟΣΜΙΑ ΚΑΤΑΝΑΛΩΣΗ % ΕΝΕΡΓΕΙΑΣ ΑΝΑ ΚΑΥΣΙΜΟ

## Slide 11: ΚΑΤΑΝΑΛΩΣΗ ΕΝΕΡΓΕΙΑΣ ΑΝΑ ΑΤΟΜΟ

## Slide 12: ΠΑΓΚΟΣΜΙΑ ΑΠΟΘΕΜΑΤΑ ΠΕΤΡΕΛΑΙΟΥ
Notes: BP AMOCO FOR 1998

## Slide 13: DISTRIBUTED GENERATION
ΔΙΕΣΠΑΡΜΕΝΗ ΗΛΕΚΤΡΟΠΑΡΑΓΩΓΗ

## Slide 14: ΔΙΕΣΠΑΡΜΕΝΟ ΔΙΚΤΥΟ ΜΕ ΣΥΜΒΑΤΙΚΗ ΠΑΡΑΓΩΓΗ

## Slide 15: ΔΙΕΣΠΑΡΜΕΝΟ ΔΙΚΤΥΟ ΜΕ ΔΙΕΣΠΑΡΜΕΝΗ ΠΑΡΑΓΩΓΗ & ΑΝΕΞΑΡΤΗΤΟ ΔΙΚΤΥΟ ΔΙΑΝΟΜΗΣ

## Slide 16: ΤΟ ΗΛΕΚΤΡΙΚΟ ΔΙΚΤΥΟ ΤΟΥ ΜΕΛΛΟΝΤΟΣ
Notes: The smarter energy network of the future, EPRI believes, will incorporate a diversified pool of resources located closer to the consumer, pumping out low- or zero-emissions power in backyards, driveways, downscaled local power stations, and even in automobiles, while giving electricity users the option to become energy vendors. The front end of this new system will be managed by third-party "virtual utilities," which will bundle electricity, gas, Internet access, broadband entertainment, and other customized energy services. (This vision is reminiscent of Edison's original ambition for the industry, which was not to sell lightbulbs, but to create a network of technologies and services that provided illumination.)
The smarter energy network of the future, EPRI believes, will incorporate a diversified pool of resources located closer to the consumer, pumping out low- or zero-emissions power in backyards, driveways, downscaled local power stations, and even in automobiles, while giving electricity users the option to become energy vendors. The front end of this new system will be managed by third-party "virtual utilities," which will bundle electricity, gas, Internet access, broadband entertainment, and other customized energy services. (This vision is reminiscent of Edison's original ambition for the industry, which was not to sell lightbulbs, but to create a network of technologies and services that provided illumination.)

## Slide 17: ΣΤΑΔΙΑ ΠΑΡΑΓΩΓΗΣ ΗΛΕΚΤΡΙΣΜΟΥ
ΚΥΚΛΟΣ ΑΤΜΟΥ ΚΑΙ ΚΑΥΣΑΕΡΙΩΝ
ΧΗΜΙΚΗ – ΠΥΡΗΝΙΚΗ
ΘΕΡΜΙΚΗ
ΜΗΧΑΝΙΚΗ
ΗΛΕΚΤΡΙΚΗ
ΥΔΡΟΗΛΕΚΤΡΙΚΗ & ΑΙΟΛΙΚΗ
ΚΙΝΗΤΙΚΗ
ΜΗΧΑΝΙΚΗ
ΗΛΕΚΤΡΙΚΗ
ΗΛΕΚΤΡΙΚΗ ΕΝΕΡΓΕΙΑ
ΙΣΧΥΣ: ΣΥΝΕΧΕΣ ΡΕΥΜΑ DC power = I * V
ΕΝΑΛΛΑΣΣΟΜΕΝΟ AC power = I * V * cos(φ)

## Slide 18: ΓΑΙΑΝΘΡΑΚΕΣ (ΚΑΡΒΟΥΝΟ)
ΤΥΡΦΗ
ΛΙΓΝΙΤΗΣ
ΥΠΟ-ΑΣΦΑΛΤΟΥΧΟΙ ΓΑΙΑΝΘΡΑΚΕΣ
ΑΣΦΑΛΤΟΥΧΟΙ ΓΑΙΑΝΘΡΑΚΕΣ
ΑΝΘΡΑΚΙΤΗΣ

## Slide 19: ΑΠΟΘΕΜΑΤΑ ΚΑΡΒΟΥΝΟΥ
ΑΣΙΑ | 259.3
Β.ΑΜΕΡΙΚΗ | 246.1
ΑΦΡΙΚΗ | 32.0
ΕΥΡΩΠΗ & ΕΥΡΑΣΙΑ | 272.2
ΚΕΝΤΡ.&ΝΟΤΙΟΣ ΑΜΕΡΙΚΗ | 15.0
ΜΕΣΗ ΑΝΑΤΟΛΗ | 1.4

## Slide 20: ΣΧΗΜΑΤΙΣΜΟΣ ΤΟΥ ΚΑΡΒΟΥΝΟΥ

## Slide 21: ΚΑΤΗΓΟΡΙΕΣ ΚΑΡΒΟΥΝΟΥ

## Slide 22: ΕΠΙΦΑΝΕΙΑΚΗ ΕΞΟΡΥΞΗ ΛΙΓΝΙΤΗ

## Slide 23: ΛΙΓΝΙΤΙΚΟΣ ΕΚΣΚΑΦΕΑΣ

## Slide 24: ΤΥΠΙΚΗ ΔΟΜΗ ΓΑΙΑΝΘΡΑΚΩΝ

## Slide 25: ΣΤΑΔΙΑ
ΕΞΟΡΥΞΗ
ΠΡΟΕΤΟΙΜΑΣΙΑ (ΠΑΡΑΓΩΓΗ ΟΜΟΓΕΝΟΠΟΙΗΜΕΝΗΣ ΠΡΩΤΗΣ ΥΛΗΣ)
ΚΑΥΣΗ
ΠΑΡΑΓΩΓΗ ΘΕΡΜΟΤΗΤΑΣ
ΠΑΡΑΓΩΓΗ ΜΗΧΑΝΙΚΗΣ ΕΝΕΡΓΕΙΑΣ
ΠΑΡΑΓΩΓΗ ΗΛΕΚΤΡΙΣΜΟΥ

## Slide 26: ΑΠΟΘΕΜΑΤΑ ΛΙΓΝΙΤΗ ΣΤΗΝ ΕΛΛΑΔΑ

## Slide 27: ΣΥΜΒΑΤΙΚΗ ΚΑΥΣΗ ΣΕ ΕΣΧΑΡΕΣ

## Slide 28: ΡΕΥΣΤΟΠΟΙΗΜΕΝΗ ΚΛΙΝΗ

## Slide 29: ΥΓΡΟΠΟΙΗΣΗ ΚΑΙ ΑΕΡΙΟΠΟΙΗΣΗ ΓΑΙΑΝΘΡΑΚΩΝ
Notes: When molecular hydrogen (H2) is added to coal at about 400 degrees Celsius, solid coal is converted to a liquid fuel that is quite similar to petroleum. This process is called coal liquefaction. Molecular hydrogen is expensive and this is a complex process. So it is not practiced anywhere in the world today. During World War II, Germany was cut off from petroleum fields and it produced all of its gasoline and jet fuel from coal. This is commercially available technology that is believed to become economically attractive when the price of a barrel of crude oil exceeds $30-35.

## Slide 30: ΑΕΡΙΟΠΟΙΗΣΗ ΓΑΙΑΝΘΡΑΚΩΝ
C + H2O = CO + H2 (στους 700 C)
Το μονοξείδιο του άνθρακα έχει το 1/3 της θερμογόνου δύναμης του φυσικού αερίου, και μπορεί να χρησιμοποιηθεί γιά την παραγωγή συνθετικής βενζίνης.
Notes: When coal is reacted with either steam (H2O) or molecular hydrogen (H2) at temperatures in excess of 700 degrees Celsius, it is converted to a gaseous fuel that is more or less similar to natural gas. This process is called coal gasification. It is also commercially available technology. It is more attractive economically than coal liquefaction, especially when steam is used in the following (simplified) reaction with coal:
C + H2O = CO + H2
The product (carbon monoxide, CO, and hydrogen, H2) can be used either as a clean gaseous fuel (having 1/3 of the heating value of natural gas) or as a raw material from which gasoline can be produced. The latter process is called 'indirect liquefaction'. That's how South Africa - with its abundant coal reserves and until recently suffering from an oil embargo - produces most of its gasoline.

## Slide 31: ΛΙΓΝΙΤΙΚΟΙ ΣΤΑΘΜΟΙ ΗΛΕΚΤΡΟΠΑΡΑΓΩΓΗΣ
Εκμετάλλευση Ιπτάμενης Τέφρας
Δέσμευση θείου κατά την καύση λόγω της περιεκτικότητας σε ασβέστιο (π.χ. λιγνίτες Πτολεμαΐδας)
Ως πρόσθετο γιά την παραγωγή ειδικών τσιμέντων ( στην Ελλάδα το ποσοστό ιπτάμενης τέφρας στο τελικό προϊόν ανέρχεται στο 10 % )
Γιά την κατασκευή ελαφρών αδρανών
Στην οδοποιΐα γιά : α) θεμελίωση οδοστρωμάτων, β) σταθεροποίηση εδαφών και στεγανοποίηση
Ως φορέας καταλυτών
Στην επεξεργασία υγρών αποβλήτων : α) δέσμευση μαγγανίου, μολύβδου, χρωμίου, φωσφωρικών ϊόντων, και ϊόντων φθορίου, β) δέσμευση φαινόλης, γ) μείωση ΒOD5 και COD
Στην κατασκευή ασβεστοπυριτικών πλίνθων και κεραμικών ειδών
Γιά εξαγωγή ιχνοστοιχείων

## Slide 32: ΠΕΤΡΕΛΑΙΟ

## Slide 33: ΠΕΤΡΕΛΑΙΟ - ΑΠΟΘΕΜΑΤΑ(2009)
ΑΣΙΑ | 42.2
Β.ΑΜΕΡΙΚΗ | 73.3
ΑΦΡΙΚΗ | 127.7
ΕΥΡΩΠΗ & ΕΥΡΑΣΙΑ | 136.9
ΚΕΝΤΡ.&ΝΟΤΙΟΣ ΑΜΕΡΙΚΗ | 198.9
ΜΕΣΗ ΑΝΑΤΟΛΗ | 754.2

## Slide 34: ΑΠΟΘΕΜΑΤΑ ΠΕΤΡΕΛΑΙΟΥ

## Slide 35: ΑΠΟΔΕΔΕΙΓΜΕΝΑ ΑΠΟΘΕΜΑΤΑ-ΥΠΟΛΕΙΠΟΥΣΑ ΠΑΡΑΓΩΓΗ

## Slide 36: ΠΡΟΣΦΟΡΑ ΚΑΙ ΖΗΤΗΣΗ

## Slide 37: ΧΑΡΤΗΣ ΠΕΤΡΕΛΑΙΑΓΩΓΩΝ ΣΤΗΝ ΕΥΡΩΠΗ

## Slide 38: oil well plan

## Slide 39: ΤΡΥΠΑΝΙΑ ΠΕΤΡΕΛΑΙΟΥ

## Slide 40: ΠΛΩΤΗ ΠΛΑΤΦΟΡΜΑ ΕΞΟΡΥΞΗΣ ΠΕΤΡΕΛΑΙΟΥ

## Slide 41: ΠΟΡΩΔΕΣ ΠΕΤΡΩΜΑ ΜΕ ΠΕΤΡΕΛΑΙΟ

## Slide 42: ΠΕΤΡΕΛΑΙΟ – ΕΓΚΛΩΒΙΣΜΟΣ ΜΕΤΑΞΥ ΑΔΙΑΠΕΡΑΣΤΩΝ ΠΕΤΡΩΜΑΤΩΝ
Notes: Oil Leg to Column
Predict downdip oil leg or displaced oil. Quantify height of original oil column for calculating volume of oil displaced.

## Slide 43: ΠΕΤΡΕΛΑΙΟ – ΕΓΚΛΩΒΙΣΜΟΣ ΣΕ ΤΑΜΙΕΥΤΗΡΕΣ

## Slide 44: Εντοπισμος γεωλογικών στρωμάτων με ηχητικά κύματα

## Slide 45: ΔΙΑΤΑΞΗ ΠΕΤΡΩΜΑΤΩΝ ΚΑΙ ΤΑΜΙΕΥΤΗΡΩΝ ΜΕΤΑΝΑΣΤΕΥΣΗ ΠΕΤΡΕΛΑΙΟΥ

## Slide 46: Άντληση πετρελαίου

## Slide 47: Άντληση πετρελαίου στην θάλασσα
Notes: (source: IFP)
Today, the potential represented by deep offshore resources has not yet been clearly determined. Sedimentary areas lying in over 200 m of water represent nearly 55 million km² of sedimentary basins, or four times the conventional offshore surface area. The permits that have already been delivered only cover 5% of this area.
Deep-offshore conditions present certain characteristics (high pressures, low temperatures, large water-depth range, the constant presence of ocean currents, etc.) that are radically different from those typifying conventional offshore operations.

## Slide 48: Τεχνολογίες γιά θαλάσσια άντληση
Notes: (source: IFP)
For oil companies, the next target depth is 3 000 m. Meeting this objective constitutes a major industry challenge for the next 5 to 10 years.
The transition from deep offshore to ultra-deep offshore will require higher allocations of R&D resources. Beyond a certain limit, it will not be possible to extrapolate from existing solutions, so new ones will have to be found and proven appropriate and reliable.

## Slide 49: install new cable on the service rig.

## Slide 50: service rig that will be used for swabbing and pump replacement

## Slide 51: Drilling Well

## Slide 52: Drilling Well

## Slide 53: Well

## Slide 54: Disposal Pit for well

## Slide 55: Drilling well

## Slide 56: Tank for well

## Slide 57: well during drilling. This well was spewing oil
Notes: eff Davis #5 well during drilling. This well was spewing oil at such a rate during drilling that the disposal pit had to be emptied twice, and the volume of oil in the drill hole almost stopped the drilling rig crew from finishing the well.

## Slide 58: ΣΥΣΤΑΣΗ ΠΕΤΡΕΛΑΙΟΥ

## Slide 59: Wooden oil derricks stretching out into California's Santa Barbara Channel
Notes: PHOTO CAPTION: Wooden oil derricks stretching out into California's Santa Barbara Channel, circa early 1900s, would be replaced by modern offshore platforms. A series of oil spills forced a moratorium on development of other potential oil and gas deposits off the coast of California.

## Slide 60: Alberta tar sands

## Slide 61: Oil Refinery
Notes: PHOTO CAPTION: Arak Oil Refinery in Iran, which is one of the world's largest oil producers. It supplies China with approximately 15 percent of the oil the Asian powerhouse imports, which gives it extraordinary political leverage despite U.S. efforts to isolated it.

## Slide 62: ΕΠΕΞΕΡΓΑΣΙΑ ΑΡΓΟΥ ΠΕΤΡΕΛΑΙΟΥ
ΑΡΓΟ ΠΕΤΡΕΛΑΙΟ
ΑΝΤΛΗΣΗ
ΜΕΤΑΦΟΡΑ
ΦΥΣΙΚΗ ΕΠΕΞΕΡΓΑΣΙΑ
ΧΗΜΙΚΗ ΕΠΕΞΕΡΓΑΣΙΑ
ΠΕΤΡΕΛΑΙΟ
ΜΑΖΟΥΤ
ΒΕΝΖΙΝΗ
ΚΗΡΟΖΙΝΗ
ΛΙΠΑΝΤΕΛΑΙΑ
ΔΙΫΛΙΣΤΗΡΙΟ

## Slide 63: ΚΛΑΣΜΑΤΙΚΗ ΑΠΟΣΤΑΞΗ ΠΕΤΡΕΛΑΙΟΥ

## Slide 64: ΚΛΑΣΜΑΤΙΚΗ ΣΤΗΛΗ ΚΑΙ CRACKING
Notes: Cracking Cracking takes large hydrocarbons and breaks them into smaller ones.
There are several types of cracking:
Thermal - you heat large hydrocarbons at high temperatures (sometimes high pressures as well) until they break apart.
  steam - high temperature steam (1500 degrees Fahrenheit / 816 degrees Celsius) is used to break ethane, butane and naptha into ethylene and benzene, which are used to manufacture chemicals.
  visbreaking - residual from the distillation tower is heated (900 degrees Fahrenheit / 482 degrees Celsius), cooled with gas oil and rapidly burned (flashed) in a distillation tower. This process reduces the viscosity of heavy weight oils and produces tar.
  coking - residual from the distillation tower is heated to temperatures above 900 degrees Fahrenheit / 482 degrees Celsius until it cracks into heavy oil, gasoline and naphtha. When the process is done, a heavy, almost pure carbon residue is left (coke); the coke is cleaned from the cokers and sold.
- uses a catalyst to speed up the cracking reaction. Catalysts include zeolite, aluminum hydrosilicate, bauxite and silica-alumina.
  fluid catalytic cracking - a hot, fluid catalyst (1000 degrees Fahrenheit / 538 degrees Celsius) cracks heavy gas oil into diesel oils and gasoline.
  hydrocracking - similar to fluid catalytic cracking, but uses a different catalyst, lower temperatures, higher pressure, and hydrogen gas. It takes heavy oil and cracks it into gasoline and kerosene (jet fuel).
After various hydrocarbons are cracked into smaller hydrocarbons, the products go through another fractional distillation column to separate them
Unification Sometimes, you need to combine smaller hydrocarbons to make larger ones -- this process is called unification. The major unification process is called catalytic reforming and uses a catalyst (platinum, platinum-rhenium mix) to combine low weight naphtha into aromatics, which are used in making chemicals and in blending gasoline. A significant by-product of this reaction is hydrogen gas, which is then either used for hydrocracking or sold.
Alteration Sometimes, the structures of molecules in one fraction are rearranged to produce another. Commonly, this is done using a process called alkylation. In alkylation, low molecular weight compounds, such as propylene and butylene, are mixed in the presence of a catalyst such as hydrofluoric acid or sulfuric acid (a by-product from removing impurities from many oil products). The products of alkylation are high octane hydrocarbons, which are used in gasoline blends to reduce knocking (see "What does octane mean?" for details).
An oil refinery is a combination of all of these units.

## Slide 65: ΤΟ CRACKING TOY ΠΕΤΡΕΛΑΙΟΥ ΣΕ ΜΙΚΡΟΤΕΡΟΥΣ ΥΔΡΟΓΟΝΑΝΘΡΑΚΕΣ
Notes: Cracking Cracking takes large hydrocarbons and breaks them into smaller ones.

## Slide 66: ΕΞΕΛΙΞΗ ΤΙΜΩΝ ΠΕΤΡΕΛΑΙΟΥ ($2005)

## Slide 67: ΤΟ ΦΥΣΙΚΟ ΑΕΡΙΟ

## Slide 68: ΦΥΣΙΚΟ ΑΕΡΙΟ
ΑΣΙΑ-ΕΙΡΗΝΙΚΟΣ | 16.24
Β.ΑΜΕΡΙΚΗ | 9.16
ΑΦΡΙΚΗ | 14.76
ΕΥΡΩΠΗ & ΕΥΡΑΣΙΑ | 63.09
ΚΕΝΤΡ.&ΝΟΤΙΟΣ ΑΜΕΡΙΚΗ | 8.06
ΜΕΣΗ ΑΝΑΤΟΛΗ | 76.18

## Slide 69: Το φυσικό αέριο – κατασκευή αγωγού

## Slide 70: ΤΟ ΦΥΣΙΚΟ ΑΕΡΙΟ ΣΤΗΝ ΕΥΡΩΠΗ

## Slide 71: ΤΟ ΦΥΣΙΚΟ ΑΕΡΙΟ ΣΤΗΝ ΕΛΛΑΔΑ

## Slide 72: ΣΥΣΤΑΣΗ ΦΥΣΙΚΟΥ ΑΕΡΙΟΥ

## Slide 73: ΡΕΒΥΘΟΥΣΑ: ΣΤΑΘΜΟΣ ΑΠΟΘΗΚΕΥΣΗΣ

## Slide 74: ΠΥΡΗΝΙΚΑ ΚΑΥΣΙΜΑ

## Slide 75: Συναρμολόγηση πυρηνικής ράβδου

## Slide 76: Πυρηνικός αντιδραστήρας

## Slide 77: Υαλοποίηση πυρηνικών αποβλήτων

## Slide 78: ΣΥΝΤΗΞΗ

## Slide 79: Σύντηξη – συγκράτηση πλάσματος

## Slide 80: Σύντηξη–ακτινοβολία πλάσματος στον αντιδραστήρα θερμοκρασία εκκίνησης 100,000,000 C
Notes: In an operating fusion reactor, part of the energy generated will serve to maintain the plasma temperature as fresh deuterium and tritium are introduced. However, in the startup of a reactor, either initially or after a temporary shutdown, the plasma will have to be heated to 100 million degrees Celsius.
In current tokamak (and other) magnetic fusion experiments, insufficient fusion energy is produced to maintain the plasma temperature. Consequently, the devices operate in short pulses and the plasma must be heated afresh in every pulse

## Slide 81: ΜΕΤΑΤΡΟΠΗ ΕΝΕΡΓΕΙΑΣ

## Slide 82: Ενεργειακή μετατροπή σε θερμικό σταθμό
ΧΗΜΙΚΗ ΕΝΕΡΓΕΙΑ ΚΑΥΣΙΜΟΥ
ΛΕΒΗΤΑΣ
ΘΕΡΜΙΚΗ ΕΝΕΡΓΕΙΑ
ΣΤΡΟΒΙΛΟΣ
ΜΗΧΑΝΙΚΗ ΕΝΕΡΓΕΙΑ
ΓΕΝΝΗΤΡΙΑ
ΗΛΕΚΤΡΙΣΜΟΣ
ΚΑΛΥΨΗ ΑΝΑΓΚΩΝ

## Slide 83: Βασική αρχή

## Slide 84: Προσπάθειες...

## Slide 85: ΚΑΥΣΗ

## Slide 86: Απόδοση καύσης και περίσσεια αέρα
Notes: Combustion Efficiency and Excess Air
Optimizing a boilers efficiency is important to minimize fuel consumption and unwanted excess to the environment
To ensure complete combustion of the fuel used, combustion chambers are supplied with excess air. Excess air increase the amount of oxygen and the probability of combustion of all fuel.
when fuel and oxygen in the air are in perfectly balance - the combustion is said to be stoichiometric
The combustion efficiency will increase with increased excess air, until the heat loss in the excess air is larger than than the heat provided by more efficient combustion.
Typical excess air to achieve highest efficiency for different fuels are
5 - 10% for natural gas
5 - 20% for fuel oil
15 - 60% for coal

## Slide 87: Μεταβολή % CO2 με την περίσσεια αέρα
Notes: Carbon dioxide - CO2 - is a product of the combustion and the content in the flue gas is an important indication of the combustion efficiency.
An optimal content of carbon dioxide - CO2 - after combustion is approximately 10% for natural gas, and approximately 13% for light oils.
Normal combustion efficiencies for natural gas at different amounts of excess air and flue gas temperatures are indicated below:

## Slide 88: Εσωτερικό θαλάμου καύσεως

## Slide 89: Παραγωγή ισχύος – σχηματική παράσταση

## Slide 90: ΗΛΕΚΤΡΟΠΑΡΑΓΩΓΗ-ΣΥΝΔΥΑΣΜΕΝΟΣ ΚΥΚΛΟΣ

## Slide 91: Αεριοστρόβιλος (1) και Ατμοστρόβιλος (2)
(1)
(2)

## Slide 92: Πυρηνικός σταθμός – σκαρίφημα

## Slide 94: ΜΗΧΑΝΕΣ
I. ΘΕΡΜΙΚΑ
  ΑΤΜΟΥ
    ΠΑΛΙΝΔΡΟΜΙΚΕΣ
    ΣΤΡΟΒΙΛΟΙ
  ΜΗΧΑΝΕΣ ΕΣΩΤΕΡΙΚΗΣ ΚΑΥΣΗΣ
  ΜΗΧΑΝΕΣ ΕΞΩΤΕΡΙΚΗΣ ΚΑΥΣΗΣ
  ΑΕΡΙΟΣΤΡΟΒΙΛΟΜΗΧΑΝΕΣ
ΙΙ. ΥΔΡΟΗΛΕΚΤΡΙΚΑ
ΙΙΙ. ΑΙΟΛΙΚΕΣ ΜΗΧΑΝΕΣ
IV. ΑΜΕΣΗΣ ΜΕΤΑΤΡΟΠΗΣ
  ΚΥΤΤΑΡΑ ΚΑΥΣΙΜΟΥ
  ΦΩΤΟΒΟΛΤΑΪΚΑ
  ΘΕΡΜΙΚΑ /ΜΑΓΝΗΤΟΥΔΡΟΔΥΝΑΜΙΚΑ/ΘΕΡΜΙΟΝΙΚΑ/ΘΕΡΜΟΗΛΕΚΤΡΙΚΑ

## Slide 95: ΑΠΟΔΟΣΗ ΜΕΤΑΤΡΟΠΗΣ
ΠΕΤΡΕΛΑΙΟ 26.6 %
ΚΑΡΒΟΥΝΟ 32.5 %
ΕΛΑΦΡΟΥ ΥΔΑΤΟΣ 24.9 %
ΗΛΙΑΚΟΣ ΣΥΛΛΕΚΤΗΣ 2.4 %
ΣΥΜΠΑΡΑΓΩΓΗ 50 %

## Slide 96: ΑΕΡΙΟΣΤΡΟΒΙΛΟΣ

## Slide 97: Τυπικοί αεριοστρόβιλοι αεροπλάνων
Notes: When you go to an airport and see the commercial jets there, you can't help but notice the huge engines that power them. Most commercial jets are powered by turbofan engines, and turbofans are one example of a general class of engines called gas turbine engines.
There are many different kinds of turbines:
You have probably heard of a steam turbine. Most power plants use coal, natural gas, oil or a nuclear reactor to create steam. The steam runs through a huge and very carefully designed multi-stage turbine to spin an output shaft that drives the plant's generator.
Hydroelectric dams use water turbines in the same way to generate power. The turbines used in a hydroelectric plant look completely different from a steam turbine because water is so much denser (and slower moving) than steam, but it is the same principle.
Wind turbines, also known as wind mills, use the wind as their motive force. A wind turbine looks nothing like a steam turbine or a water turbine because wind is slow moving and very light, but again, the principle is the same.
A gas turbine is an extension of the same concept. In a gas turbine, a pressurized gas spins the turbine. In all modern gas turbine engines, the engine produces its own pressurized gas, and it does this by burning something like propane, natural gas, kerosene or jet fuel. The heat that comes from burning the fuel expands air, and the high-speed rush of this hot air spins the turbine.
Advantages and Disadvantages So why does the M-1 tank use a 1,500 horsepower gas turbine engine instead of a diesel engine? It turns out that there are two big advantages of the turbine over the diesel:
Gas turbine engines have a great power-to-weight ratio compared to reciprocating engines. That is, the amount of power you get out of the engine compared to the weight of the engine itself is very good.
Gas turbine engines are smaller than their reciprocating counterparts of the same power.
The main disadvantage of gas turbines is that, compared to a reciprocating engine of the same size, they are expensive. Because they spin at such high speeds and because of the high operating temperatures, designing and manufacturing gas turbines is a tough problem from both the engineering and materials standpoint. Gas turbines also tend to use more fuel when they are idling, and they prefer a constant rather than a fluctuating load. That makes gas turbines great for things like transcontinental jet aircraft and power plants, but explains why you don't have one under the hood of your car.

## Slide 98: ΣΤΡΟΒΙΛΟΣ-ΓΕΝΝΗΤΡΙΑ

## Slide 99: ΣΤΡΟΒΙΛΟΣ 2 ΣΤΑΔΙΩΝ

## Slide 100: Αεριοστρόβιλος με θάλαμο καύσης
Notes: THE GAS-TURBINE PRIMER
This section is provided as an educational service to people of all ages and professions who are interested in gas-turbine operation and theory. We feel it is in the best interest of the gas-turbine industry to educate the general population about this technology since it is a major power source used in the generation of electricity, and the power plant of choice for modern aircraft and way-cool boats.
GAS-TURBINE THEORY
A simple gas turbine is comprised of three main sections a compressor, a combustor, and a turbine. The gas-turbine operates on the principle of the Brayton cycle, where compressed air is mixed with fuel, and burned under constant pressure conditions. The resulting hot gas is allowed to expand through a turbine to perform work. In a 33% efficient gas-turbine approximately two / thirds of this work is spent compressing the air, the rest is available for other work ie.( mechanical drive, electrical generation)

## Slide 101: Αεριοστρόβιλος με θάλαμο καύσης και αναγέννηση (ανάκτηση θερμότητας)
Notes: One variation of this basic cycle is the addition of a regenerator. A gas-turbine with a regenerator (heat exchanger) recaptures some of the energy in the exhaust gas, pre-heating the air entering the combustor. This cycle is typically used on low pressure ratio turbines.

## Slide 102: Αεριοστρόβιλος με ενδιάμεση ψύξη του αέρα (ανάμεσα στα στάδια)
Notes: Gas-turbines with high pressure ratios can use an intercooler to cool the air between stages of compression, allowing you to burn more fuel and generate more power. Remember, the limiting factor on fuel input is the temperature of the hot gas created, because of the metallurgy of the first stage nozzle and turbine blades. With the advances in materials technology this physical limit is always climbing.

## Slide 103: Αεριοστρόβιλος με αναθέρμανση

## Slide 104: ΑΕΡΙΟΣΤΡΟΒΙΛΟΣ ΜΕ ΑΝΑΚΤΗΣΗ ΘΕΡΜΟΤΗΤΑΣ

## Slide 105: An Intercooled & Recuperated Turbine
Notes: An Intercooled & Recuperated Turbine

## Slide 106: ΑΕΡΙΟΣΤΡΟΒΙΛΟΣ ΜΕ ΕΓΧΥΣΗ ΑΤΜΟΥ ΓΙΑ ΜΕΙΩΣΗ ΝΟχ
Notes: The arrangement is known as the steam-injected-gas-turbine (STIG) and has the added advantage of reducing the nitrogen oxide (NOx) emissions because the
combustion temperature is lowered.

## Slide 107: Βενζινοκινητήρας-σχηματικό διάγραμμα τροφοδοσίας

## Slide 108: Μηχανή bypass

## Slide 109: Στοιχεία τούρμπο-τζέτ μηχανής

## Slide 110: Θάλαμος καύσης αεριοστροβίλου αεροσκάφους

## Slide 111: ΜΗΧΑΝΕΣ ΕΣΩΤΕΡΙΚΗΣ ΚΑΥΣΗΣ

## Slide 112: Μηχανή εσωτερικής καύσης

## Slide 113: 2 – χρονη μηχανή εσωτ.καύσης

## Slide 114: Πύργοι ψύξης γιά θερμικούς σταθμούς

## Slide 115: Πύργος ψύξεως

## Slide 116: Σχηματική παράσταση σταθμού με πύργο ψύξεως

## Slide 117: Πύργος ψύξης (εσωτερικό)
Notes: An Introduction to Cooling Tower Drift In the cooling tower, hot water is sprayed over contact media called fill as air is drawn counter current or cross current to the water stream. As the water is sprayed and evaporated, a large distribution of droplet sizes is created. A portion of these droplets will become entrained in the exit air stream and leave the cooling tower. These droplets are referred to as drift. These drift droplets and the solids they contain will be deposited downwind of the cooling tower. Significant emission and deposition can lead to icing, transformer shorts, environmental degradation, and environmental non-compliance. Inertial impaction devices called drift eliminators are used to control the emission of these drift droplets. High efficiency drift eliminators of modern design can potentially control the drift to less than 0.0005 % of the cooling tower circulating water flow. These drift eliminators are able to capture nearly 100% of the droplets which are larger than 10 microns in diameter. However, large droplets up to 1000 microns may still be generated by cooling towers. The sources of these droplets include:
Gaps in the drift eliminators - The drift eliminators must be installed around cooling tower structural members. This is usually accomplished by cutting the drift eliminator to fit. The cut portion of the drift eliminator does not have the same particle capture characteristics as the unaltered drift eliminator. Any gap left between the drift eliminator and the structural member or wall is also a source of uncontrolled emission. Typically air seals are installed to prevent drift from passing the drift eliminator between the drift eliminator and the wall.
Variations in local air velocities - Modern drift eliminators are designed for a fairly wide range of air velocities. If the local velocity is not within the design band, the drift rate may be increased.
Re-entrainment of collected drift - Cooling tower structural members, the surface of the fan stack and the cooling tower fan blades collect drift droplets. Water accumulated on these surfaces can be re-entrained in the air. Since these surfaces are downstream of the drift eliminators, the droplet size is determined by the entrainment process and the local velocity. The local air velocity must be greater than the settling velocity in order for emission to occur. Re-entrainment from the drift eliminators can also occur although this is usually caused by overloading due to a malfunction of the cooling tower water distribution system.
Emission from such sources may comprise most of the mass of the drift emitted by cooling towers. Cooling towers with high efficiency drift eliminators are able to achieve their low drift rates because the emission of drift through the drift eliminators is actually much lower than the nominal rate. Since the generation of the larger drift droplets is a function of the details of the cooling tower design as well as the quality of the installation of the drift eliminators, the prediction of the size distribution of the drift for a cooling tower yet to be built is subject to great uncertainty

## Slide 118: ΚΑΤΑΚΡΑΤΗΣΗ CO2

## Slide 119: Εκπομπές CO2 1900-1990

## Slide 120: ΑΠΟΜΑΚΡΥΝΣΗ CO2
ΣΕ ΕΞΑΝΤΛΗΜΕΝΟ ΤΑΜΙΕΥΤΗΡΑ ΠΕΤΡΕΛΑΙΟΥ Η ΦΥΣΙΚΟΥ ΑΕΡΙΟΥ (ή ΓΙΑ ΤΗΝ ΑΝΤΛΗΣΗ ΤΟΥ ΠΕΤΡΕΛΑΙΟΥ)
ΣΕ ΠΑΛΙΟ ΟΡΥΧΕΙΟ
ΣΤΗΝ ΘΑΛΑΣΣΑ

## Slide 121: ΑΠΟΜΑΚΡΥΝΣΗ CO2
Notes: DIRECT INJECTION INVOLVES THE CAPTURE, SEPARATION, TRANSPORT, AND INJECTION OF CARBON DIOXIDE INTO THE DEEP SEA
"At great depths, CO2 is denser than sea water, and it may be possible to store it on the bottom as liquid or deposits of icy hydrates," Bishop explains. "At depths easy to reach with pipes, CO2 is buoyant; it has to be diluted and dispersed so it will dissolve."
What happens to carbon dioxide introduced into the ocean in this way may soon be field-tested in Hawaii. Over a two-week period researchers plan to inject 40 to 60 metric tons of pure liquid CO2 over 2,500 feet deep in the ocean near the Big Island.
One variable they will be measuring is acidity. Water and carbon dioxide form carbonic acid, "but once diluted in sea water, carbonic acid is not the dominant chemical species," Bishop says, "because of seawater's high alkalinity and buffering capacity." If calcium carbonate sediments are involved, acidity is even less. "Think of Tums," he suggests.

## Slide 122: Αποθήκευση CO2 σε εξαντλημένη πετρελαιοπηγή

## Slide 123: Αποθήκευση CO2 σε ταμιευτήρα

## Slide 124: ΕΠΕΞΕΡΓΑΣΙΑ ΚΑΥΣΑΕΡΙΩΝ

## Slide 125: ΣΧΗΜΑΤΙΣΜΟΣ ΝΟx

## Slide 126: KAΥΣΗ ΣΤΑΓΟΝΑΣ ΠΕΤΡΕΛΑΙΟΥ ΣΕ ΜΙΚΡΟΒΑΡΥΤΗΤΑ

## Slide 127: Μικροφωτογραφία ιπτάμενης τέφρας

## Slide 128: ΚΑΥΣΑΕΡΙΑ ΕΠΕΞΕΡΓΑΣΙΑ 1

## Slide 129: ΚΑΥΣΑΕΡΙΑ ΕΠΕΞΕΡΓΑΣΙΑ 2

## Slide 130: Θερμικός σταθμός με επεξεργασία καυσαερίων

## Slide 131: Σταθμός με αποθείωση- σχηματική διάταξη λειτουργίας

## Slide 132: ΣΥΓΧΡΟΝΟΣ ΘΕΡΜΙΚΟΣ ΣΤΑΘΜΟΣ

## Slide 133: ΑΝΑΝΕΩΣΙΜΕΣ ΠΗΓΕΣ ΕΝΕΡΓΕΙΑΣ ΚΑΙ ΤΕΧΝΟΛΟΓΙΑ

## Slide 134: ΑΝΑΝΕΩΣΙΜΕΣ ΠΗΓΕΣ ΕΝΕΡΓΕΙΑΣ
ΓΕΩΘΕΡΜΙΑ
ΚΥΜΑΤΙΚΗ
ΗΛΙΑΚΗ
ΒΙΟΜΑΖΑ
ΑΙΟΛΙΚΗ
ΥΔΡΑΥΛΙΚΗ ΕΝΕΡΓΕΙΑ

## Slide 135: ΓΕΩΘΕΡΜΙΑ
Γεωθερμική κλίμακα 1 οC/ 30m
Αβαθής γεωθερμία

## Slide 136: Θερμοκρασιακή τομή της Γης

## Slide 137: Γεωθερμικές περιοχές

## Slide 138: Γεωθερμικές περιοχές στην Ευρώπη

## Slide 139: Γεωθερμία: Σχηματική παράσταση

## Slide 140: Γεωθερμική γεώτρηση

## Slide 141: Εναλλάκτης γεωθερμικής θερμότητας

## Slide 142: Γεωθερμικός σταθμός

## Slide 143: Γεωθερμικός σταθμός ξηρού ατμού

## Slide 144: Ηλιακή ενέργεια

## Slide 145: McDonnell Douglas (currently Boeing) SD system

## Slide 146: Θερμοηλεκτρικό σύστημα ηλιακής ενέργειας Stirling Energy Systems, Inc. (SES)/Boeing, 25 kW SD system at sunset.

## Slide 147: Ηλιακό θερμικό σύστημα αέρα

## Slide 148: Ηλιακό σύστημα παραγωγής με φωτοβολταϊκά

## Slide 149: Συγκεντρωτικό ηλιακό κάτοπτρο

## Slide 150: Ηλιακός θερμικός σταθμός-Γαλλία

## Slide 151: Ηλιακός θερμικός σταθμός

## Slide 152: ΠΥΡΓΟΣ ΕΣΤΙΑΣΗΣ

## Slide 153: Ηλιακός θερμοηλεκτρικός σταθμός

## Slide 154: Βιοκλιματική αρχιτεκτονική

## Slide 155: ΗΛΙΑΚΟ ΣΠΙΤΙ

## Slide 156: ΒΙΟΚΛΙΜΑΤΙΚΟ ΣΠΙΤΙ - ΤΕΝΕΡΙΦΗ

## Slide 157: ΒΙΟΚΛΙΜΑΤΙΚΟ ΣΠΙΤΙ-

## Slide 158: ΒΙΟΚΛΙΜΑΤΙΚΟ ΣΠΙΤΙ -

## Slide 159: ΒΙΟΚΛΙΜΑΤΙΚΟ ΣΠΙΤΙ-ΦΥΤΕΜΕΝΗ ΣΤΕΓΗ

## Slide 160: ΒΙΟΚΛΙΜΑΤΙΚΟ ΣΠΙΤΙ: ΕΛΛΑΔΑ

## Slide 161: Αιολική ενέργεια

## Slide 162: Αιολικός Ατλας Ευρώπης

## Slide 164: Ανεμογεννήτρια 1650 W

## Slide 165: Ανεμογεννήτρια – σχηματική τομή

## Slide 166: Κατανομή πίεσης στην πτέρυγα

## Slide 167: Ανεμογεννήτρια - συναρμολόγηση

## Slide 168: Αιολική ανεμογεννήτρια στην Ολλανδία

## Slide 169: ανεμογεννήτρια

## Slide 170: Ενσωματώση στο περιβάλλον

## Slide 171: Αιολικό πάρκο

## Slide 172: Αιολικό πάρκο στην Καλιφόρνια

## Slide 173: Αιολικό πάρκο

## Slide 174: Εγκατάσταση στην θάλασσα

## Slide 175: Μικρό οικιακό σύστημα

## Slide 176: Μικρό υβριδικό σύστημα

## Slide 177: Υδροηλεκτρική ενέργεια

## Slide 178: Εξάτμιση θερμού επιφανειακού νερού και δημιουργία βροχής στην ξηρά.
Notes: Evaporation of warm surface water increases the amount of moisture in the colder, drier air flowing immediately above the lake surface. With continued evaporation, water vapor in the cold air condenses to form ice-crystal clouds, which are transported toward shore

## Slide 179: Υδρολογικός κύκλος

## Slide 180: Φράγμα, αγωγοί, σταθμός, κατάντη ποταμού

## Slide 181: Υδροηλεκτρικό φράγμα

## Slide 182: Κίνα – Το μεγάλο φράγμα

## Slide 183: Κατάντη του φράγματος

## Slide 184: ΣΥΣΤΗΜΑ ΥΔΡΟΣΤΡΟΒΙΛΟΥ-ΓΕΝΝΗΤΡΙΑΣ

## Slide 185: Υδροηλεκτρικός σταθμός-σχηματική παράσταση

## Slide 186: ΥΔΡΟΣΤΡΟΒΙΛΟΣ

## Slide 187: Τροχός Pelton

## Slide 188: ΚΥΜΑΤΙΚΗ ΕΝΕΡΓΕΙΑ

## Slide 189: Αρχή της παλινδρομούσας στήλης
Principles of the Oscillating Water Column

## Slide 190: Βασική αρχή

## Slide 191: Τομή κυματικού σταθμού

## Slide 192: Κυματικός σταθμός

## Slide 193: Κυματικός σταθμός

## Slide 194: Κυματικός σταθμός

## Slide 195: Κυματική μηχανή

## Slide 196: Κυματική γεννήτρια
The Turbo Generator
500kW Turbo-Generator for LIMPET

## Slide 197: κατασκευή

## Slide 198: ΑΠΟΘΗΚΕΥΣΗ ΕΝΕΡΓΕΙΑΣ

## Slide 199: Ηλεκτρισμός και θερμότητα δύσκολο να αποθηκευτούν
Υλικά αλλαγής φάσης
Νερό
Βότσαλα
Υδραυλική ενέργεια
Μπαταρία
Περιστρεφόμενη μάζα
Υδρογόνο με ηλεκτρόλυση

## Slide 200: Γιατί χρειάζεται η αποθήκευση ηλεκτρισμού

## Slide 201: Fly-wheel γιά αποθήκευση ενέργειας
Notes: A Flywheel Energy Storage System consists of a rotating cylinder (rim) suspended on magnetic bearings in a vacuum and connected to a motor/generator. The motor/generator transforms electrical energy into stored kinetic energy by spinning a 150-pound composite rim up to a speed of 700 meters per second. The flywheel is able to spin for extended periods with great efficiency, because friction and drag are virtually eliminated by employing magnetic bearings and a vacuum system.
When the product is called upon to produce electricity (see flywheel in action), the spinning flywheel drives the motor/generator, that instantaneously converts the kinetic energy into electrical energy. This conversion continues, and the flywheel slows, until it is "discharged.«
Flywheel in Action Follow the flywheel through its three modes of operation: 1. Flywheel Charge Mode
AC power is supplied to the Flywheel Controller
Controller powers up the Flywheel to full speed within one hour
2. Flywheel Float Mode 3. Flywheel Discharge Mode

## Slide 202: Λειτουργία περιστρεφόμενου δίσκου
Notes: Flywheel in Action Follow the flywheel through its three modes of operation: 1. Flywheel Charge Mode 2. Flywheel Float Mode 3. Flywheel Discharge Mode
AC power is disrupted
Flywheel supplies power to the Controller
Controller provides uninterrupted power to the Customer Load
Flywheel speed decreases

## Slide 203: Κυψέλη καυσίμου για φορητές συσκευές
Notes: Μια μικρή κυψέλη καυσίμου της Toshiba θα μπορούσε να αντικαταστήσει τις μπαταρίες στις φορητές ηλεκτρονικές συσκευές από το 2005. Η κυψέλη χρησιμοποιεί μεθανόλη και μπορεί να τροφοδοτήσει ένα mp3 player για 20 ώρες, με μόλις 2ml καυσίμου.
Παρόμοιες κυψέλες καυσίμου που λειτουργούν με υδρογόνο, με μεθάνιο ή μεθανόλη αναμένεται να κάνουν από του χρόνου την εμφάνισή τους και σε φορητούς υπολογιστές. Η NEC έχει ήδη παρουσιάσει έναν πειραματικό φορητό με ενσωματωμένη κυψέλη.
Οι κυψέλες καυσίμου είναι ηλεκτρομηχανικές συσκευές στις οποίες η ενέργεια από χημικές αντιδράσεις μετατρέπεται απευθείας σε ηλεκτρισμό. Τα παραπροϊόντα είναι μόνο διοξείδιο του άνθρακα και νερό, καθιστώντας τις κυψέλες καυσίμου πιο φιλικές για το περιβάλλον.
Το πρωτότυπο που παρουσίασε η Toshiba στην Ιαπωνία έχει μέγεθος 2,2 επί 4,5 εκατοστά και ζυγίζει 8,5 γραμμάρια. «Είναι αρκετά μικρή ώστε να ενσωματωθεί σε ασύρματα ακουστικά για κινητά τηλέφωνα, αλλά αρκετά αποδοτική ώστε να τροφοδοτεί ένα mp3 player για 20 ώρες με ένα και μόνο γέμισμα με δύο χιλιοστόλιτρα μεθανόλης υψηλής συγκέντρωσης» δήλωσε εκπρόσωπος της εταιρείας στο Γαλλικό Πρακτορείο Ειδήσεων.
Η κυψέλη αναμένεται να περάσει στην παραγωγή το 2005, η τιμή της όμως δεν έχει ακόμα καθοριστεί.

## Slide 204: Κύτταρο καυσίμου

## Slide 205: Κύτταρο καυσίμου

## Slide 206: Κύτταρο καυσίμου

## Slide 207: Η δομή της πολυμερούς ηλεκτρολυτικής μεμβράνης
Τα κύτταρα καυσίμου πολυμερούς ηλεκτρολυτικής μεμβράνης περιορίζονται από το θερμοκρασιακό εύρος στο οποίο το νερό είναι υγρό. Η μεμβράνη θα πρέπει να περιέχει νερό ώστε τα ιόντα υδρογόνου να μπορούν να μεταφέρουν το φορτίο μέσα στην μεμβράνη. Η λειτουργία τους σε θερμοκρασίες που υπερβαίνουν τους 100 oC είναι δυνατή μόνον κάτω από συνθήκες πίεσης, ώστε να διατηρείται η υγρή φάση του νερού

## Slide 208: Κύτταρο καυσίμου

## Slide 209: Το σύστημα αποθήκευσης ενέργειας REGENESYS
Notes: Block diagram of the Regenesys™ energy storage system

## Slide 210: Σύστημα κύτταρων καυσίμου
Notes: A single regenerative fuel cell, showing electrolyte and electrical connections
Regenerative fuel cell plants store or release electrical energy by means of a reversible electrochemical reaction between two salt solutions (the electrolytes). The reaction occurs within an electrochemical cell. The cell has two compartments, one for each electrolyte, physically separated by an ion-exchange membrane. In contrast to most types of battery system, the electrolytes flow into and out of the cell through separate manifolds and are transformed electrochemically inside the cell, as shown in illustration two

## Slide 211: Επαλληλία συστημάτων αποθήκευσης
Notes: Economies of scale and manufacture can be achieved by linking cells together, with an electrode shared between two cells. The cathode of one cell becomes the anode of another. This is known as bipolar module. The Regenesys™ system uses a number of bipolar modules (illustration three) linked electrically in series to form a string with the required dc bus voltage. The electrolytes are distributed to the modules in parallel through manifolds

## Slide 212: Κοσμική ακτινοβολία – ΤΟ ΤΕΛΟΣ
Notes: Origin of the cosmic background radiation
About 100,000 years after the Big Bang, the temperature of the Universe had dropped sufficiently for electrons and protons to combine into hydrogen atoms, p + e --> H. From this time onwards, radiation was effectively unable to interact with the background gas; it has propagated freely ever since, while constantly losing energy because its wavelength is stretched by the expansion of the Universe. Originally, the radiation temperature was about 3000 degrees Kelvin, whereas today it has fallen to only 3K.
Observers detecting this radiation today are able to see the Universe at a very early stage on what is known as the `surface of last scattering'. Photons in the cosmic microwave background have been travelling towards us for over ten billion years, and have covered a distance of about a million billion billion miles. The Origin of Fluctuations in the CBR
There are a variety of competing theories for the origin of large-scale structure and the fluctuations in the cosmic microwave background radiation. These models fall into two categories: (1) causal topological defect models, such as cosmic strings and textures, or (2) inflationary scenarios.