## Slide 1
Defining the Coastal Zone:
Theory, Methods & Application on Islands
ISLAS Summer School Lesvos 2026
Efi Chatzi

## Slide 2
Why Does the Definition Matter?
"Show me your coastal zone boundary and I will show you your planning philosophy"
What is included?
A narrow definition may leave out coastal-related development. A very broad one may include areas unnecessarily.
Who is responsible?
The boundary affects which authority and which laws apply
What is protected?
Ecosystems such as Posidonia meadows, dunes and wetlands need to be inside the defined zone to be visible in planning.
What do we measure?
Built-up change results depend on where the coastal zone is drawn.

## Slide 3
01
Theoretical Frameworks: What is the Coastal Zone?

## Slide 4
Competing Definitions in the Literature
ICZM Protocol (Barcelona Convention, 2008)
Coast as a connected land–sea system Ecosystems, resources, communities and activities interact.
UNEP/MAP (2011)
Coast as an interface A transition zone shaped by natural processes and human activities.
EU Directive 2014/89 (MSP)
No fixed coastal-zone definition Focuses on land–sea interactions and coordination.
EEA / Copernicus (operational)
Operational definition Uses administrative regions or fixed buffers for data analysis.

## Slide 5
Three Approaches to Coastal Zone Delineation
Fixed Buffer
✓ Pros:
Simple, reproducible, comparable
✗ Cons:
Ignores terrain and local context
Use:
Quick comparisons, national/statistical studies
Examples:
500 m, 10 km, 50 km buffers
Administrative
✓ Pros:
Matches governance and available data
✗ Cons:
Borders are not always coastal in reality
Use:
Policy monitoring, socio-economic statistics
Examples:
Coastal municipalities, NUTS3 regions
Multi-criteria
✓ Pros:
More realistic for islands
✗ Cons:
Needs more data and GIS work
Use:
Detailed planning and impact analysis
Examples:
Rhodes method: elevation + buffers + contours + settlements (Chatzi et al. 2025b)

## Slide 6
02
Policy Framework: ICZM, MSP & Greek Law

## Slide 7
ICZM: Integrated Coastal Zone Management
ICZM Principles (Barcelona Protocol, 2008)
Integrated view of the coast
Land–sea connection
Multi-actor governance
Adaptive management
Sustainable development
Precautionary principle
Legal Framework
2002
EC Recommendation 2002/413
Promotes ICZM principles in Europe.
2008 / 2011
Barcelona ICZM Protocol
Adopted in 2008 and entered into force in 2011 Mediterranean framework for integrated coastal management.
2014
EU Directive 2014/89/EU - Maritime Spatial Planning
Requires maritime spatial plans and land–sea interaction.
2001
Greek Law 2971/2001
Defines and protects the seashore and beach.
ICZM treats the coast as a connected and dynamic land–sea system, not simply as a narrow strip along the shoreline

## Slide 8
03
Operational Method: The Multi-Criteria Approach

## Slide 9
Multi-Criteria Delineation: The Rhodes Method
A
Elevation < 50m
+ 500m buffer
Flat coastal land, more exposed to development and flooding.
B
Elevation ≥ 50m
+ 200m buffer
Elevated coastal terrain. Smaller buffer because pressure is usually lower.
C
Settlements
+ 500m buffer
Coastal settlements are included even if they extend beyond the physical buffer.
D
5m contour
+ 1,000m buffer
Very low-lying areas, useful for flood risk and wetlands.

## Slide 10
Coastal Typologies: The Result
INSIDE settlements
OUTSIDE settlements
Flat terrain
< 50m elevation
Semi-flat terrain
≥ 50m elevation
Urban Flat Coastal Zone
+16.4%
EX-URBAN FLAT
COASTAL ZONE ⚠
+41% main sprawl area
Urban Semi-Flat Coastal Zone
Stable
Ex-urban Semi-Flat Coastal Zone
Small contribution

## Slide 11
Implementing the Coastal Zone in GIS
1
Load coastline (HMGS 1:5,000)
Use the official shoreline as the reference geometry for all buffer operations.
2
Generate buffers: 200m, 500m, 1,000m
QGIS: Vector → Geoprocessing → Buffer. Use "EPSG:2100" (metres). Dissolve = yes.
3
Load DEM → Reclassify elevation
Raster → Raster Calculator: DEM < 50 = 1 (flat); DEM ≥ 50 = 2 (semi-flat). Polygonize result.
4
Extract 5m isoline
From DEM: Raster → Extraction → Contour. Set interval = 5. Use only the 5m isoline.
5
Load settlement boundaries
From e-Poleodomia or digitised from topographic maps. CRS: EPSG:2100.
6
Apply four spatial criteria
Intersect each criterion with the elevation reclassification and settlement layer. Union all four results.
7
Create coastal typologies
Overlay elevation class × settlement status within the coastal zone. Five typologies emerge from the combination.

## Slide 12
Group Assignment: Coastal Zone Part
1. Justify your approach
Explain why you chose fixed buffer / administrative / multi-criteria. What are the analytical implications for your island group?
2. Data sources
List all datasets used. Where did you get the coastline? DEM? Settlement boundaries? Note any quality issues or gaps.
3. Map the coastal zone
Present a clear map showing the delineated zone against the island geography. Show typologies if using multi-criteria approach.
4. Compare with policy zones
How does your coastal zone relate to existing protected areas (Natura 2000), settlement limits, national shoreline protection?
5. Identify limitations
No definition is perfect. What does your approach miss? What would you do differently with more data or time?

## Slide 13
Summary: Coastal Zone Definition
There is no single coastal-zone definition. The choice depends on the question.
Definitions can be simple or complex. Buffer, administrative, or multi-criteria.
Policy matters. ICZM, MSP and Greek law shape how the coast is managed.
Multi-criteria methods are useful for islands. They combine distance, elevation and settlements.
The main planning concern: Flat coastal land outside settlements, the typical sprawl zone.